## Slide 1: Dual Reaction Wheel Updates
Yuen Bak Ching, Clay Dodson, Ethan Kee, and Alexander Sun

## Slide 2: Problem Statement
Create a Reaction Wheel Pendulum which uses flywheels to stabilize itself
Will start and remain upright (θ < 10o)
Can accept light disturbances (F < 10N)
Adjusts to weights being added (up to 5g)

## Slide 3: System Model and EoM
Can use Lagrange’s equations:
Generalized coordinate qi is pendulum and reaction wheel angles, θ and ϕ
𝜏i is the total torque acting at each point

## Slide 4: State Space Model

## Slide 5: The Control Law
q1 = 1/500 (pendulum angular velocity )
q2 = 1/100 (flywheel angle )
q3 = 1/5000 (flywheel angular velocity )
R = 1/100
Final LQR Gains: [0.8597, 0.1342, 0.0432]

## Slide 6: Simulation

## Slide 7: Hardware Selection
Sensor selection criteria: Able to have both accelerometer and gyroscope
MPU-6050 Accelerometer and Gyroscope
Actuator selection criteria: High torque, with encoder
2x UXcell DC 12V 350 RPM Encoder Gear Motors
MCU: MSP432P401R

## Slide 8: Initial Design

## Slide 9: The Final Build

## Slide 10: Non-Linearity Problems Encountered
Motor-deadzone
  Motor doesn’t move when angle is too small (calculated duty cycle is too small)
Rate-Limit
  Motor cannot physically accelerate as fast as we would like it to
  After implementing rate-limiter, motor is required to exceed saturation limit
Saturation Limit
  Motor is barely powerful enough
  Exceeds saturation limit after rate-limiter is implemented

## Slide 11: Problems
The non-linearity problems
IMU data is corrupted by the magnetic field generated by motor
  Attempted to use aluminium foil to shield IMU (makeshift faraday’s cage)
Ground noise
Flywheel initially not large enough (Moment of Inertia too small)
  Bigger and heavier flywheel installed (10x the moment of inertia)

## Slide 12: Conclusion
Use shielded wire for wiring IMU to attempted to eliminate EMI
Select a motor with smaller dead-zone
Find a way to deal with motor dead-zone effectively