## Slide 1: ME 4405 – FINAL PROJECT
Hand motion mimicking RRR robot
Juan Munoz and Yuen Bak CHING

## Slide 2: IDEATION
A robot arm with 3-dof modelled after the human arm
Human arm with sensors (accelerometer) to detect arm movements
Robot Mimic the human arm’s final position

## Slide 3: PERFORMANCE REQUIREMENT
Accurately mimics the position of the wrist of the person
Relatively stable, can counteract disturbances(PID controller)

## Slide 4: SYSTEM DESIGN

## Slide 5: SYSTEM ALGORITHM
Sensor: Accelerometer
Compute positions (by integration)
Compute joint angles (by RDA)
Send to Motors
Obtain actual angle (from motor encoder)
PID controller

## Slide 6: P CONTROLLER FOR BRUSHLESS MOTOR
Reason: I and D control introduce too many delays causes system to behave erratically

## Slide 7: CONTROLLER GAIN
Calculate motor constant experimentally

## Slide 8: HOME-MADE ROBOT ARM
Reason: Want to try use Brush-Less motor instead of servo, more challenging
Built using oak (cheap, sturdy, lightweight)
Home-made motor mount and hub to reduce weight and cost(less sturdy but working)
Pulley system to avoid fastening motor to joints, thus decreasing required torque

## Slide 9: CIRCUIT DIAGRAM (ORIGINAL)
Too complex, too ambitious

## Slide 10: CIRCUIT DIAGRAM (MODIFIED)

## Slide 11: Things to Improve (1)
Motor burnt out after hours of testing
  Servo Motor should be way easier in this project (too ambitious)
Code did not prevent possible singular configurations
  Some hard stop in code can be implemented but time ran out
Cannot control pathing of robot arm (limitation of RDA)
Code did not prevent possible singular configurations
  Some hard stop in code can be implemented but time ran out

## Slide 12: Things to Improve (2)
Accelerometer data grows out of bounds (robot ends to restart from time to time)
  Data integrated, thus error is accumulating
  Should use gyroscope as well and use a filter to combine both data
I2C data corrupted by motor’s magnetic interference
  Either use shielded cables or introduce a grounded metal shield

## Slide 13: WHAT IT ACHIEVED?
P controller working and constantly adjusting and holding arm in place
Successfully obtain accurate positions from accelerometer (by integration)
Using such position to calculate joint angles (robotics -> RDA)
Robot motion greatly resembles arm motion